TPS2Mouse

This module has been created because in a standard PS2 mouse there are two encoders (x, y) and two buttons and if it is one of the Intelli Mouse type it will have three encoders (x, y, z) and three (or five buttons), which gives many potential uses and the management of them is done outside of the board. Two pins are required, clock and data pins, to control the mouse and although any pin would be valid, the maximum number of mice has been limited to 3 (the limit can easily be changed by modifying the following line
#define MAX_MICE 0x03
in the file FirmataPS2Mouse.h for a higher value).

You need to install a new library in the Arduino IDE and the code for the new module in ConfigurableFirmata, The library for Arduino is based on these two (github.com/kristopher/PS2-Mouse-Arduino y rucek/arduino-ps2-mouse) with little changes. The installation of this library is done in the usual way, downloading the file "ps2-mouse.zip" from the "arduino code" part and installing it in the Arduino IDE, the necessary part for ConfigurableFirmata is in "src.zip" and you have to copy it into "src" folder of ConfigurableFirmata and finally you have to add some lines in the file "ConfigurableFirmata.ino" to work with the new module.

After the lines
#include <FirmataScheduler.h>
FirmataScheduler scheduler;
you have to add these
#include <PS2Mouse.h>
#include <FirmataPS2Mouse.h>
FirmataPS2Mouse ps2mouse;

in the procedure and after
firmataExt.addFeature(scheduler);
add
firmataExt.addFeature(ps2mouse);
and finally in the loop() procedure inside the if (reporting.elapsed ()) {
...
ps2mouse.report();
}

The main properties are:
Board: Instance of the board to which it belongs.
DataPin, ClockPin: pins used for communication with the mouse.
Device: mouse number, from 0 to 2 (more changing MAX_MICE).
MouseType: mouse type, one of (STANDARD, INTELLI_MOUSE, FIVEBUTTONS, STILL_UNKNOWN).
MouseData: record with the last mouse reading.
Status: stores the last value of the read Status record, not to be confused with MouseData status.
Scaling: one of (PS2MOUSE_SCALING_1_TO_1, PS2MOUSE_SCALING_2_TO_1).
Mode: one of (PS2MOUSE_STREAM, PS2MOUSE_REMOTE).
Resolution: one of (PS2MOUSE_1_COUNT_MM, PS2MOUSE_2_COUNT_MM, PS2MOUSE_4_COUNT_MM, PS2MOUSE_8_COUNT_MM).
SampleRate: one of (R_10, R_20, R_40, R_60, R_80, R_100, R_200).
Reporting: configures the automatic mouse position reading mode.

ClockPin and DataPin are checked only when Enabled True to activate the corresponding instance, showing an error if this is the case, it is also checked if the pin is assigned to another TPin instance or belongs to an active module. The instance is activated with the following default values, PS2MOUSE_REMOTE, PS2MOUSE_8_COUNT_MM, R_60 and SCALING_1_TO_1.

In this momment only REMOTE mode is allowed.

Valid commands are:
config, set clock, data pins an initial mode.
0 START_SYSEX (0xF0)
1 PS2MOUSE_DATA (0x50)
2 PS2MOUSE_CONFIG (0x02)
3 mouse number (0-3)
3 ClockPin (0-127)
4 DataPin (0-127)
5 Mode (optional) REMOTE 1, STREAM 0
5/6 END_SYSEX (0xF7)
        queryStatus, query status register from mouse.
        0 START_SYSEX (0xF0)
1 PS2MOUSE_DATA (0x50)
 2 PS2MOUSE_STATUS (0x01)
 3 Mouse number (0-2)
 4 END_SYSEX (0xF7)
queryDeviceID, query connected mouse type.
0 START_SYSEX (0xF0)
 1 PS2MOUSE_DATA (0x50)
 2 PS2MOUSE_DEVICEID (0x03)
 3 Mouse number (0-2)
 4 END_SYSEX (0xF7
queryData, query record position and button states.
0 START_SYSEX (0xF0)
1 PS2MOUSE_DATA (0x50)
2 PS2MOUSE_DATA (0x50)
3 Mouse number (0-2)
4 END_SYSEX (0xF7)
reset, init the mouse.
0 START_SYSEX (0xF0)
 1 PS2MOUSE_DATA (0x50)
2 PS2MOUSE_RESET (0x00)
3 Mouse number (0-2)
4 END_SYSEX (0xF7)
sendSampleRate, set mouse sample rate.
0 START_SYSEX (0xF0)
1 PS2MOUSE_DATA (0x50)
2 PS2MOUSE_SET_SAMPLE_RATE (0x05)
3 Mouse number (0-2)
4 sample rate lsb
5 sample rate msb
6 END_SYSEX (0xF7)
sendResolution, set mouse resolution.
0 START_SYSEX (0xF0)
1 PS2MOUSE_DATA (0x50)
2 PS2MOUSE_SET_RESOLUTION (0x04)
3 Mouse number (0-2)
4 resolution (0-3)
5 END_SYSEX (0xF7)
sendReporting, enable/disable automatic reporting mouse position.
0 START_SYSEX (0xF0)
1 PS2MOUSE_DATA (0x50)
2 PS2MOUSE_REPORTING (0x06)
3 Mouse number (0-2)
4 Reporting (0-1) 1 enable, 0 disable, it is firmata reporting not mouse reporting
5 END_SYSEX (0xF7)
sendFiveButtonsMode, special INTELLI MOUSE mode with five buttons, but wheel move is only 4 bits.
0 START_SYSEX (0xF0)
 1 PS2MOUSE_DATA (0x50)
 2 PS2MOUSE_SET_FIVE_BUTTONS (0x07)
 3 Mouse number (0-2)
 5 END_SYSEX (0xF7)
sendRemoteMode, set mouse in REMOTE mode.
0 START_SYSEX (0xF0)
 1 PS2MOUSE_DATA (0x50)
 2 PS2MOUSE_SET_REMOTE_MODE (0x09)
 3 Mouse number (0-2)
 5 END_SYSEX (0xF7)

Response data
queryDeviceID response,
0 START_SYSEX (0xF0)
  1 PS2MOUSE_DATA (0x50)
  2 PS2MOUSE_DATA (0x50)
  3 Mouse number (0-2)
  4 Mouse Type (0-127) 0 = standard, 3 = intelli_mouse, 4 = five buttons
  5 END_SYSEX (0xF7)
queryStatus response,
 0 START_SYSEX (0xF0)
1 PS2MOUSE_DATA (0x50)
        2 PS2MOUSE_STATUS (0x01)
        3 Mouse number (0-2)
        4 status (lsb) //Status bits: bit 7: always 0; bit 6: Mode: 1 remote, 0 stream; bit 5: enable internal reporting
        5 status (msb) //bit 4: scaling; bit 3: always 0; bit 2: middle button; bit 1:right button; bit 0: left button
        6 Resolution (lsb)
        7 Resolution (msb)
        8 SampleRate (lsb)
        9 SampleRate (msb)
        10 END_SYSEX (0xF7)
queryData response,
    0 START_SYSEX (0xF0)
    1 PS2MOUSE_DATA (0x50)
    2 PS2MOUSE_DATA (0x50)
     3 Mouse number (0-2)
     4 status (lsb) //Status bits: bit 7: y overflow; bit 6: x overflow; bit 5: y sign; bit 4: x sign;
     5 status (msb) //bit 3: always 1; bit 2: middle button; bit 1:right button; bit 0: left button
     6 x position (lsb)
     7 x position (msb)
     8 y position (lsb)
     9 y position (msb)
     10 wheel (lsb) // three buttons mode: bit 0-7: wheel move
     11 wheel (msb) // five buttons mode: bit 5: five button; bit 4: four button; bit 0-3: wheel move
     12 END_SYSEX (0xF7)

The OnMouseData event is activated with the queryData request or when the Reporting property is True, giving the mouse position data and the buttons status.
The OnMouseDeviceID event is activated with the queryDeviceID request and returns the mouse type.