TAccelStepper

This module manages most of stepper types, you can mix them on the same board but be careful or you will be run out of memory.

The main properties are:
Board: Instance of the plate to which it belongs.
Device: device number, from 0 to 9.
MotorPin1_or_DriverStep: Pin for motor 1 or direct driver pin.
MotorPin2_or_DriverDirection: Pin for motor 2 or pin address.
Motor Pin3: Pin for motor 3.
Motor Pin4: Pin for motor 4.
MotorEnablePin: Pin to enable or disable the stepper.
InvertMotorPin1, InvertMotorPin, etc.: if a motor pin works in inverted mode.
InterfaceType: one of (ACCEL_INTERFACE_DRIVER, ACCEL_INTERFACE_2_WIRE, ACCEL_INTERFACE_3_WIRE, ACCEL_INTERFACE_4_WIRE).
StepSize: one of (WHOLE_STEP, HALF_STEP).
Speed: floating point value, steps per second.
Acceleration: floating point value max is 1000000.
Steps: motor steps to be performed.

MotorPins are checked only when trying to activate the corresponding instance, showing an error if it is the case, it is also checked if the pin is assigned to another TPin instance or belongs to an active module. The instance is activated with the speed and acceleration properties.

The OnStepperPosition event is triggered by the ReportPosition request and the OnStepperMoveCompleted event each time a movement ends.

When the Acceleration and Speed ​​properties are modified in an activated instance (Enabled = true), these changes are sent to the stepper (there is no need to call the setAcceleration or setSpeed ​​functions).

Stop: this function stops the stepper with the programmed acceleration (see problems with this function in ConfigurableFirmata below).
FastStop: this function has been implemented to achieve a fast stepper stop speed, is implemented by changing the acceleration to maximum, then calls the Stop function and finally selects the normal acceleration again.

In AccelStepper of ConfigurableFirmata the Stop function is programmed in the file AccelStepperFirmata.ccp in the following way:

else if (stepCommand == ACCELSTEPPER_STOP)
{
   if (stepper [deviceNum])
  {
   stepper [deviceNum] -> stop ();
   isRunning [deviceNum] = false;
   reportPosition (deviceNum, true);
  }
}

The function performs an instant stop but when the engine is started again it starts with the last speed and maximum acceleration, it does not start in accelerated mode.

Changing the source code in the way below, stepper stops in a decelerated mode and the next start uses the programmed acceleration.

Source code changes, in the file AccelStepperFirmata.ccp comment the last two lines of the block:

else if (stepCommand == ACCELSTEPPER_STOP)
{
   if (stepper [deviceNum])
  {
   stepper [deviceNum] -> stop ();
   // isRunning [deviceNum] = false; // line to comment
   // reportPosition (deviceNum, true); // line to comment
  }
}

Until this problem is solved and it is decided how to implement the STOP function, the component TAccelStepper supposed you have compiled AccelStepperFirmata with those lines commented doing a decelerated stop.
But if you want an instant stop, the TAccelStepper has implemented a FastStop function, it works in this way, setting a very large acceleration (actually the maximum allowed) then send the STOP command (with this maximum deceleration) and then reconfigure the preprogrammed acceleration.