TI2C

This module manages the pin assignments for calls of two wire communications, I2C type. Although the I2C module of ConfigurableFirmata does not yet support 10 bit communications on this bus, it has been prepared when they are available.

The main properties are:
Board: Instance of the board to which it belongs.
Delay: optional delay after config.
SDApin and SCLpin: they are read only at this time because the bus management is done by the chip itself and has dedicated pins.

SDApin and SCLpin are checked if the pins are in use only when trying to activate the corresponding instance, showing an error if it were the case.

Important events:
OnI2CData: reports the requested data to a device.

The OnEnabled events are executed after activating the instance and OnDisabled after deactivating.

The most important functions:
Read: it sends a read request, due to the size of the buffer of the I2C functions and the limitation of the size of data to be sent, there can only be a maximum of about 28 bytes in each call. RandomRead: sends a read request on a certain address, same limitation as Read. ReadContinuously: Read a record continuously.
StopReading: Stop the continuous reading.
WriteData: write data on the bus, the maximum amount is limited as in the Read function.

There are the same functions for 10-bit devices but they are not yet supported in ConfigurableFirmata.

Once an instance has been deactivated, it is checked if it has ReadContinuously active events and if this is the case it stops them.