TServo

This module manages the assignments of a pin to control a servo.

The main properties are:
Board: Instance of the board to which it belongs.
Pin: Pin used for the module.
Device: Identifier of the servo connected to the board.
MinPulse: minimum pulse size for the servo, default to 544.
MaxPulse: minimum pulse size for the servo, default to 2400.
Value: value to position the servo, see servo in Arduino.

Pin is checked only when trying to activate the corresponding instance, showing an error if it was the case, it is also checked if the pin is assigned to another instance or belongs to an active module.
When a servo is activated with Enabled to true, it is configured with the MinPulse and MaxPulse properties and is positioned according to the value of the Value property.

The OnEnabled event are executed after activating the instance and OnDisabled after deactivating.