TAccelStepper

This module manages most of stepper types controlled by two, three or four pins, you can mix them on the same board it can have accelerated start, plus an optional activation pin.
The main properties are:
Board: Board instance to which it belongs.
Device: device number, from 0 to 9.
MotorPin1_or_DriverStep: Pin for motor 1 or direct driver pin.
MotorPin2_or_DriverDirection: Pin for motor 2 or direction pin.
MotorPin3: Pin for motor 3.
MotorPin4: Pin for motor 4.
MotorEnablePin: Pin to activate or deactivate the motor.
InvertMotorPin1, etc: Whether a motor pin works in inverted mode.
InterfaceType: One of ACCEL_INTERFACE_DRIVER, ACCEL_INTERFACE_2_WIRE, ACCEL_INTERFACE_3_WIRE, ACCEL_INTERFACE_4_WIRE.
StepSize: one of WHOLE_STEP, HALF_STEP.
Speed: floating point value.
Acceleration: maximum floating point value 1000000, 0.0 means 1000000.
Steps: motor steps to perform.
MotorPins are checked only when the instance is activated setting Enabled to True, displaying an error if necessary, it is also checked if any pin is already assigned. The instance is activated with the properties speed and acceleration.
If motor is running then Running read-only property is True.
When Enabled is set to false, if motor is running first it is stopped with the Stop function.
OnStepperPosition event is activated with the ReportPosition request and OnStepperMoveCompleted event each time a movement ends.
When Acceleration and Speed properties are changed in an activated instance (Enabled = true) those changes are sent to the motor (there is no need to call the setAcceleration or setSpeed functions).
Move and MoveTo functions, (in this version), do not automatically enable or disable MotorEnablePin.
Stop: this function stops the motor with the programmed acceleration (see problems with this function in ConfigurableFirmata below).
FastStop: this function has been implemented to achieve a fast engine stop, it is implemented by calling the Stop function and changing the acceleration to maximum, once stopped it recovers its previous acceleration.
In ConfigurableFirmata AccelStepper the Stop function is programmed in the AccelStepperFirmata.ccp file as follows:

else if (stepCommand == ACCELSTEPPER_STOP) {
        if (stepper[deviceNum]) {
        stepper[deviceNum]->stop();
        isRunning[deviceNum] = false;
        reportPosition(deviceNum, true);
        }
    }
The function performs an instantaneous stop but when the motor is restarted it does with the last speed and maximum acceleration, a deccelerated stop is done changing source code in this way commenting out last line and changing the previous statement to true:
else if (stepCommand == ACCELSTEPPER_STOP) {
        if (stepper[deviceNum]) {
        stepper[deviceNum]->stop();
        isRunning[deviceNum] = true;
        // reportPosition(deviceNum, true);
        }
      }