TFrequency
This module manages the frequency measurements on a pin, in AVR they can only be pins 2 or 3.
The main properties are:
Board: Board instance to which it belongs.
Pin: Pin used for the module.
Device: Identifier of the servo connected to the board, property read-only.
InterruptMode: Interrupt mode for detection.
SamplingInterval: Time during which it is sampled, by default 100 ms.
Pin is checked only when trying to activate the corresponding instance, displaying an error if this is the case, it is also checked if the pin is assigned to another instance or belongs to an active module.
OnFrequencyData event is fired every time the SamplingInterval time is met and returns the elapsed time and the number of detections.
OnEnabled events are executed after the instance is activated and OnDisabled after the instance is deactivated.