TI2C

This module manages I2C type communications (although the I2C module of ConfigurableFirmata does not yet support 10-bit communications over this bus, although it has been prepared for when they are available). Currently only one I2C instance per Tboard is allowed.

The main properties are:
Board: Instance of the board to which it belongs.
Delay: optional delay after some operations.
SDApin and SCLpin: they are especific pins for each device, on Arduino Uno are pin 18(A4) and 19 (A5), on the esp8266 are pins 4 and 5.

SDApin and SCLpin are checked if the pins are in use only when trying to activate the corresponding instance, showing an error if it were the case.

Important events:
OnI2CData: reports the requested data to a device.

OnEnabled event is executed after activating the instance and OnDisabled after deactivating.

The most important functions:
Read: it sends a read request, due to the size of the buffer of the I2C functions and the limitation of the size of data to be sent, there can only be a maximum of about 28 bytes in each call. RandomRead: sends a read request on a certain address, same limitation as Read. ReadContinuously: Read a record continuously.
StopReading: Stop the continuous reading.
WriteData: write data on the bus, the maximum amount is limited as in the Read function.

Once an instance has been deactivated, it is checked if it has ReadContinuously active events and if this is the case it stops them.