TNeopixel

This module manages the Adafruit_NeoPixel library, only one pin is needed but the maximum number of modules has been limited to 3 (you can change the limit easily by modifying the following line
#define MAX_NEOPIXELS 0x03
in the file “FirmataNeopixel.h” for a higher value and the line
     MAX_NEOPIXELS = 3;
in the file “firmataconstants.pas”).

You need to install Adafruit_NeoPixel library (https://github.com/adafruit/Adafruit_NeoPixel) and “FirmataNeopixel.zip” with the code for the new module in ConfigurableFirmata from “arduino code/Libraries to Install”, and finally you have to add the line
#define PIN_MODE_NEOPIXEL 0x12 // pin configured for NeoPixel
in the file "ConfigurableFirmata.h" and increase the value of the line
#define TOTAL_PIN_MODES 18

Main properties are:
Board: Instance of the plate to which it belongs to.
Pin: pin used for communication with the LEDs.
PixelsNumber: number of LEDs on the strip.
Device: NeoPixel module number, from 0 to 2 (expandable with MAX_NEOPIXELS).
FadeWait: number of "Sampling Interval" that must wait to change an automatic fade step, by default it is 1, which corresponds approximately to a frequency of 25 Hz, which is the speed of the human eye.
FadeRunning: when the property is written, stops or executes the last configured fading, if it is read indicates if it is running or finished.
Gamma: gamma correction of color values, applies to all.
Brightness: Brightness of all leds, 0 = maximum, 1 = minimum, 255 is one below the maximum, see details in Adafruit_Neopixel.
LedColors: order and number of colors RGBW, RGB, etc, see details in Adafruit_Neopixel.
KHZ400: transmission speed, if false is 800 Khz.

Pin are checked only when Enabled True is done to activate the corresponding instance, showing an error if that were the case, it is also checked if the pin is assigned to another TPin instance or belongs to an active module. The instance is activated with the following default values: LedColors = GRB, Gamma = 1, Brightness = 0, FadeRunning = false, FadeWait = 1, FadeColor = 0; Fade set to strip, Shift set to strip, right, wrap and show.

The orders accepted by ConfigurableFirmata are:
config, configures pin and initial data. .
0 START_SYSEX (0xF0)
1 NEOPIXELS_DATA (0x51)
2 NEOPIXELS_CONFIG (0x01)
3 device (0-3)
4 Pin (0-127)
5 NumberLeds lsb(14 bits max)
6 msb
7 LedType lsb (9 bits) //bit 8 = KHZ400, bits 7-0 'RGBW' position;
8 msb
9 END_SYSEX (0xF7)
off, turn off all led of the strip.
0 START_SYSEX (0xF0)
1 NEOPIXELS_DATA (0x51)
2 NEOPIXELS_OFF (0x00)
3 device (0-3)
4 END_SYSEX (0xF7)
show, show all the led of the strip.
0 START_SYSEX (0xF0)
1 NEOPIXELS_DATA (0x51)
2 NEOPIXELS_SHOW (0x02)
3 device (0-3)
4 END_SYSEX (0xF7)
pixelColor, sets the color of a led.
0 START_SYSEX (0xF0)
1 NEOPIXELS_DATA (0x51)
2 NEOPIXELS_SET_PIXEL (0x03)
3 device (0-3)
4 Pixel Number lsb
5 msb
6 colorRGBW blue = bits 7-0
7 encoded 7 bits green = bits 15-8
8 5 bytes red = bits 23-16
9 white = bits 31-24 of color
10 do_show = bit32, =1 show =0 not show, bit32 is bit4 of 5th byte
11 END_SYSEX (0xF7)
fillsegment, fill a piece of the strip with a color.
0 START_SYSEX (0xF0)
1 NEOPIXELS_DATA (0x51)
2 NEOPIXELS_FILL_SEGMENT (0x07)
3 device (0-3)
4 colorRGBW blue = bits 7-0
5 encoded 7 bits green = bits 15-8
6 5 bytes red = bits 23-16
7 white = bits 31-24 of color
8 do_show = bit32, =1 show =0 not show, bit32 is bit4 of 5th byte
9 First pixel lsb optional, default set to 0
10 msb
11 last pixel lsb optional, set to last pixel strip
12 msb
9..13 END_SYSEX (0xF7)
shiftSegmentConfig, configures the shift of a piece of the strip.
0 START_SYSEX (0xF0)
1 NEOPIXELS_DATA (0x51)
2 NEOPIXELS_SHIFT_CONFIG (0x06)
3 device (0-3)
4 First pixel lsb optional, default set to 0
5 msb
6 Last pixel lsb optional, set to last pixel strip
7 msb
8 shift_type optional bit0 direction, bit1 wrap, bit2 do_show, default to 0b111, right, wrap, do_show
4/9 END_SYSEX (0xF7)
shiftRun, executes a shift step, allows to change the direction.
0 START_SYSEX (0xF0)
1 NEOPIXELS_DATA (0x51)
2 NEOPIXELS_SHIFT_RUN (0x09)
3 device (0-3)
4 shif_type optional bit0 direction, bit1 wrap, bit2 do_show, default to 0b111, right, wrap, do_show
4/5 END_SYSEX (0xF7)}
fadeConfig, configure fade.
0 START_SYSEX (0xF0)
1 NEOPIXELS_DATA (0x51)
2 NEOPIXELS_FADE_CONFIG (0x08)
3 device (0-3)
4 colorRGBW blue = bits 7-0
5 encoded 7 bits green = bits 15-8
6 5 bytes red = bits 23-16
7 white = bits 31-24 of color
8
9 First pixel lsb, optional, default set to 0
10 msb
11 Last pixel lsb, optional, set to last pixel strip
12 msb
13 loops wait optional (0-15) default to 1, if SamplingRate is 19, 1 is about 25 hz eye speed
9..14 END_SYSEX (0xF7)}
fadeOneStep, execute one fade step.
0 START_SYSEX (0xF0)
1 NEOPIXELS_DATA (0x51)
2 NEOPIXELS_FADE_ONE_STEP (0x0A)
3 device (0-3)
4 do_show optional (0-1) 1=show, default not show
4/5 END_SYSEX (0xF7)}
fadeRunPause, starts or stops automatic fade.
0 START_SYSEX (0xF0)
1 NEOPIXELS_DATA (0x51)
2 NEOPIXELS_FADE_RUN_PAUSE (0x04)
3 device (0-3)
4 run/pause (0-1) 1 fade run, 0 fade pause
5 END_SYSEX (0xF7)}
sendBrightness, send brightness value to all leds.
0 START_SYSEX (0xF0)
1 NEOPIXELS_DATA (0x51)
2 NEOPIXELS_SET_BRIGHTNESS (0x05)
3 device (0-3)
4 brightnes lsb brightness value bits0-7, bit8 do_show
5 msb
6 END_SYSEX (0xF7)
movePixels, moves count leds from src to dest.
0 START_SYSEX (0xF0)
1 NEOPIXELS_DATA (0X51)
2 NEOPIXELS_MOVE_PIXELS (0x0B)
3 device (0-3)
4 src pixel lsb, source pixel
5 msb
6 dest pixel lsb, destination pixel
7 msb
8 count lsb (optional), pixels to move, default to 1
9 msb
10 do_show optional (0-1), default to not show
8..11 END_SYSEX (0xF7)}

Color can be entered by its red, green, blue and white components or directly with an integer, FillStrip functions are derived from FillSegment, shiftStripConfig derives from ShiftSegmentConfig and FadeStripConfig derives from FadeSegmentConfig.
OnFadeEnd event is activated when the fade has reached its end.