TPin

This module manages each pin that exists on the board, so you can create as many TPin instances as pins on the board.
The main properties are:
Board: Board instance.
Pin: pin number on the board
Mode: Mode in which the pin will act, one of (PIN_MODE_INPUT, PIN_MODE_OUTPUT, PIN_MODE_ANALOG, PIN_MODE_PWM, PIN_MODE_PULLUP), the other pin modes do not work with TPin, only with its corresponding module.
Pin and Mode are checked only when trying to activate the corresponding instance, displaying an error if this is the case, it is also checked if the pin is assigned to another TPin instance or belongs to an active module.
When a pin is activated in an input mode, the report pin is activated, leaving the Reporting property to true, if this property is True, the reports are received with OnPinValue event.
Reporting mode can be disabled/enabled with the ReportPin(False/True) function.
The State and Value properties return the last value written to and read from the pin.
To write a pin value, WriteValue function is used if the pin is configured in one of the output modes, the value to write depends on the mode and value is automatically adjusted according to resolution in that mode.
OnPinState event is fired with the askPinState function, which returns the mode and state of the pin.
OnEnabled event is executed right after the instance is activated and OnDisabled is executed after the instance is deactivated.
When a TPin instance is deactivated, it checks if there is any active pin report, if it is active it is deactivated before deactivating the module.